## Slide 1: Assessing Surface and Groundwater Interactions Between the Middle Brazos River Alluvium Aquifer and the Brazos River
Mark G.F. Nickels
Advisor Dr. Joe Yelderman
September 12th 2024 Board Presentation
Notes: Thank both Dr. Joe, Alan and BVGWCD

## Slide 2: Overview
Review
Study Site Updates
Data Collected
Review of Project Timeline
Further Plans

## Slide 3: Purpose and Motivation
The Brazos River, Brazos River Alluvium Aquifer (BRAA), and bedrock aquifers are a vital resource in central Texas.
Current modeling of the BRAA has been based on limited data for understanding the heterogeneity of a compartmentalized aquifer with complex interactions.

## Slide 4: Better define the interactions between Brazos River and the BRAA
What are the impacts of high or low water in the Brazos River?
What is the difference in water chemistry between the river and alluvium?
What is the influence of seasonality?
What is the influence of pumping (irrigation)?

## Slide 5: Local Study Sites
Calvert
  Coordinate river level with AquaStrategies stream measurements
Hearne
  USGS stream gauge
Bryan
  USGS stream gauge

## Slide 6: Data Loggers

## Slide 7: Local Study Site: Calvert
TLC Datalogger
LT Datalogger

## Slide 8: Local Study Site: Hearne
TLC Datalogger
LT Datalogger
Notes: Quantify the river elevation change

## Slide 9: Local Study Site: Bryan
LT Datalogger
TLC Datalogger
Notes: USGS Hearne (FM 485) on April 17th at 12am - 209.49 + 18.3 ft = 227.79
USGS Bryan (Hwy 210) on April 17th at 12 am – 188.78 + 10.89 ft =199.67
Distance = ~30mi with ~ 30ft change, ~ 1ft per mile

## Slide 10: Local Study Site: Bryan
Notes: Flip the hydrographs for presentation flow

## Slide 11
Local Study Site: Bryan Field Data
May - June
High river level
Gradient appears reversed
  Need higher accuracy elevation for wells
  Need to confirm river drop over the site

## Slide 12
Local Study Site: Bryan Field Data (Stage A)
High river level
Gradient is partially reversed

## Slide 13
Local Study Site: Bryan Field Data (Stage B)
High river level
Gradient is fully reversed

## Slide 14
Local Study Site: Bryan Field Data (Stage C)
Medium river level (falling)
Gradient returns to partially reversed

## Slide 15
Local Study Site: Bryan Field Data (Stage D)
River level continues to fall
Gradient suggests flow to the middle well
Represents a change between river to aquifer and aquifer to river

## Slide 16
Local Study Site: Bryan Field Data (Stage E)
River and middle well intertwined
Gradient from the aquifer to the river

## Slide 17
Local Study Site: Bryan Field Data (Stage F)
High river level
Gradient is partially reversed

## Slide 18: Data Collected: Historical

## Slide 19: Timeline
Task | Fall ‘23 | Spring ‘24 | Summer ‘24 |  | Fall ’24 | Sprin’24
Literature Review |  |  |  |  |  | 
River Sampling |  |  |  |  |  | 
Aquifer Sampling |  |  |  |  |  | 
Data Analysis |  |  |  |  |  | 
Report and Thesis Composition |  |  |  |  |  | 

## Slide 20: Further Plans:
At each location:
  River Sampling
  Aquifer Chemistry Sampling
  Bank Flow Measurements
Present at the National GSA conference

## Slide 21: Further Plans: River Sampling
At each location:
Water chemistry samples
  Ionic chemistry
  Isotope
Field measurements
  Temperature
  Dissolved Oxygen (DO)
  Specific Conductance (SpC)
  pH
Field alkalinity titrations

## Slide 22: Methods: Bank flow Data
Mini-Piezometers
  Hydraulic gradient between the riverbed sediment and the river
Seepage meters
  Flow into or out of the riverbed sediments
  K values
Multiple repetitions
dh
dl
Steel Drum
Plastic Bag

## Slide 23: Methods: Groundwater Sampling
At each location:
Water level
  Sonic and steel tape/E-Line
Water chemistry samples
  Ionic chemistry
  Isotope
Field measurements (bucket flow cell)
  Temperature
  Dissolved Oxygen (DO)
  Specific Conductance (SpC)
  pH
Field alkalinity titrations
Notes: So far we have sampled 52 wells, mostly in pairs of bedrock wells and BRAA.
Highlight key findings

## Slide 24: Acknowledgements
Alan Day, Brazos Valley GCD
Vivian Yale, Baylor University
Wayne Hamilton, Baylor University
Dr. Joe Yelderman, Baylor University
AquaStrategies
Landowners: Will Vaughn, Mark Hoelscher, and Laura de Asarta

## Slide 25: References
Scholarly Work
Cronin, J. G., & Wilson, C. A. (1976). Groundwater in the Flood-Plain Alluvium of the Brazos River, Whitney Dam to Vicinity of Richmond, Texas. Texas Water Development Board, Report 41(March 1967), 12–16.
Ewing, J. E., Jevon, P. E., Harding, J., Jones, T. L., Griffith, C., Freese, J. S. A., et al. (2016a). Final Conceptual Model Report for the Brazos River Alluvium Aquifer Groundwater Availability Model Texas Water Development Board.
Databases
Texas Water Development Board Groundwater Database, 1999, available at (http://www.twdb.state.tx.us/GwRD/waterwell/well_info.asp)
U.S. Department of the Interior and U.S. Geological Survey, USGS Surface-Water Daily Data for the Nation, 2023, available at (https://waterdata.usgs.gov/nwis/dv?)

## Slide 26: Questions
mark_nickels1@baylor.edu

## Slide 27: Data Collected: River Isotopes
Chart: Brazos River Isotope Ratios
| -0.28175755555555426 | -3.7848444444446017E-2 | -0.36918800000000296 | -0.68180066666666761 | -0.43341088888888812 | -0.70064244444444412 | -0.69616177777777466 | -0.33276822222222258
 | -3.8279 | -2.7539 | -3.5228 | -4.1037 | -5.0361 | -3.8355 | -5.2932 | -4.0238

## Slide 28: Data Collected: River vs Aquifer Chem.