## Slide 1: Status of Water Levels compared to Desired Future Conditions 2026
July 15, 2026
Brazos Valley
Groundwater Conservation District

## Slide 2: Groundwater Management Area 12

## Slide 3: The Texas Groundwater Planning Cycle
MAG
GCDs
GMAs
DFCs
Joint Groundwater Planning
Regional Water Planning
TWDB
MAG
Region G
Strategies
$$
GCDs

## Slide 4
Desired future condition means a quantitative description, adopted in accordance with Section 36.108, of the desired condition of the groundwater resources in a management area at one or more specified future times.
Water level decline
Volume remaining
Available drawdown remaining
Spring discharge
Water quality
Subsidence

## Slide 5: Why track DFCs?
Sec. 36.3011 (b) An affected person may file a petition with the commission requesting an inquiry for any of the following reasons:
(6) a district fails to update its rules to implement the applicable desired future conditions……
(7) the rules adopted by a district are not designed to achieve the adopted desired future conditions;
(9) the groundwater in the management area is not adequately protected due to the failure of a district to enforce substantial compliance with its rules.

## Slide 6: Some Potential Monitoring Challenges
Sufficient monitoring locations in each aquifer
Good geographic well distribution
Access to wells
Identifying screened intervals in wells
Collecting consistent measurements (pump downtime)
Even “static” measurements in confined aquifers are sensitive
Incorporating changes in monitoring network
Maintaining monitoring wells for long periods
Back-estimating water levels to starting time

## Slide 7: Desired Future Conditions
BVGCD worked with 4 other GCDs in GMA-12 to establish DFCs for 2070
DFCs adopted by GMA 12 on November 30, 2021
TWDB published MAGs on November 1, 2022 (GAM RUN 21-017 MAG)
Sparta, Queen City, Carrizo, Calvert Bluff, Simsboro, Hooper, Yegua, Jackson and Brazos River Alluvium aquifers
All DFCs changed from 2016 cycle except for Brazos River Alluvium Aquifer
DFCs result from both science and policy factors/decisions
DFCs are generally long-term goals for larger areas
Proposed DFCs for the 2026 Planning Cycle have been developed by GMA 12
The BVGCD DFC baseline date has been updated from 2000 to 2010 for the Sparta, Queen City, Carrizo, Calvert Bluff, Simsboro and Hooper aquifers

## Slide 8: DFC Development versus DFC Tracking
DFC Development
  As a part of Joint Planning Process, water level declines are evaluated by simulating the effects of pumping in GMA 12 with the GAM
  DFCs are decided in part by this modeling and other policy decisions
DFC Tracking
  Actual water level measurements are used to compare aquifer conditions to DFCs
  Use static artesian head declines in wells taken at generally the same time each year to estimate aquifer conditions for comparison to the DFC
  For Brazos River Alluvium – convert water level measurements to percent aquifer saturation
  House Bill 2078 requires Groundwater Conservation Districts to set interim values to check if they are on track to meet long-term DFC goals

## Slide 9: Current BVGCD DFC Tracking Methods
Arithmetic average of data
Spatially weighted average
  Use interpolation method to estimate data onto a regularly-spaced grid
  Average the grid values

## Slide 10: DFC Goals Established During GMA 12 2021 Planning Cycle and Proposed DFC Goals for the GMA 12 2026 Planning Cycle
Aquifer | Current BVGCD-DFC, ft (2000 – 2070) | Proposed BVGCD-DFC, ft (2010 – 2080)
Sparta | 53 | 57
Queen City | 44 | 46
Carrizo | 84 | 84
Calvert Bluff | 111 | 119
Simsboro | 262 | 330
Hooper | 167 | 146
Yegua-Jackson | 67* | 68
* Current Yegua-Jackson DFC is from 2010 - 2070

## Slide 11
Monitoring of groundwater pumping essential in understanding changes in artesian head and the status of aquifer conditions compared to DFCs
Brazos River Alluvium
Sparta Aquifer
Queen City Aquifer
Carrizo Aquifer
Calvert Bluff Formation
Simsboro Aquifer
Hooper Formation
Yegua-Jackson Aquifer
Additional Observation Well in BVGCD Monitoring Program
State Well Number
Artesian Head Change in Well
Between about 1999 and 2026, ft
+ = Increase in Artesian Head
- = Decline in Artesian Head
BVGCD Sparta Observation Well
DFC Well Map – Aquifer Key
Sparta Aquifer Example:
59-22-509
-21

## Slide 12: Sparta Aquifer DFC Wells
State Well Number | Owner
59-06-606 | Private
59-06-903 | Private
59-13-803 | Private
59-14-505 | Private
59-14-709 | Private
59-15-102 | Private
59-21-201 | City of Bryan Well 6
59-21-511 | Private
59-21-705 | TAMU Well 2
59-22-509 | Miramont County Club Well 2
59-22-512 | Private
Arithmetic Average | 11 Feet (Decline)
Spatially Weighted Average | 9 Feet (Decline)
Average Artesian Head Change 2000-2026
Arithmetic Average | 3 Feet (Increase)
Spatially Weighted Average | 6 Feet (Increase)
Average Artesian Head Change 2010-2026
2070 DFC | 53 Feet (Decline)

## Slide 13: Sparta Aquifer
Average Artesian Head Change 2000-2026
Average Artesian Head Change 2010-2026
2000-2026
Arithmetic Average: 11 feet (Decline)
Spatially Weighted Average: 9 feet (Decline)
2010-2026
Arithmetic Average: 3 feet (Increase)
Spatially Weighted Average: 6 feet (Increase)
DFC (2070):
53 feet Decline

## Slide 14: Spatially Weighted Sparta Aquifer Head Change Estimate
BVGCD Sparta Aquifer
Weighted Average Artesian Head Change 2000-2026:
9 feet (Decline)

## Slide 15: Sparta Aquifer Observation Wells
SWN = State Well Number
SI(ft) = Screened Interval, feet
TD(ft) = Total Depth, feet
2010

## Slide 16: Queen City Aquifer DFC Wells
State Well Number | Well Owner
59-05-101 | Private
59-05-905 | Private
59-06-901 | Private
59-20-935 | Private
Arithmetic Average | 8 Feet (Decline)
Spatially Weighted Average | --
Average Artesian Head Change 2000-2026
Arithmetic Average | 3 Feet (Decline)
Spatially Weighted Average | --
Average Artesian Head Change 2010-2026
2070 DFC | 44 Feet (Decline)

## Slide 17: Queen City Aquifer
Average Artesian Head Change 2000-2026
Average Artesian Head Change 2010-2026
2000-2026
Arithmetic Average: 8 feet (Decline)
Spatially Weighted Average: --
2010-2026
Arithmetic Average: 3 feet (Decline)
Spatially Weighted Average: --
DFC (2070):
44 feet Decline

## Slide 18: Queen City Aquifer Observation Wells
SWN = State Well Number
SI(ft) = Screened Interval, feet
TD(ft) = Total Depth, feet
2010

## Slide 19: Carrizo Aquifer DFC Wells
State Well Number | Well Owner
59-04-708 | Private
59-05-105 | Private
59-05-301 | Private
59-21-402 | TAMU Well 5
59-21-416 | City of College Station Carrizo #1
Arithmetic Average | 21 Feet (Decline)
Spatially Weighted Average | 19 Feet (Decline)
Average Artesian Head Change 2000-2026
Arithmetic Average | 19 Feet (Decline)
Spatially Weighted Average | 17 Feet (Decline)
Average Artesian Head Change 2010-2026
2070 DFC | 84 Feet (Decline)

## Slide 20: Carrizo Aquifer
Average Artesian Head Change 2000-2026
Average Artesian Head Change 2010-2026
2000-2026
Arithmetic Average: 21 feet (Decline)
Spatially Weighted Average: 19 feet (Decline)
2010-2026
Arithmetic Average: 19 feet (Decline)
Spatially Weighted Average:17 feet (Decline)
DFC (2070):
84 feet Decline

## Slide 21: Carrizo Aquifer Observation Wells
SWN = State Well Number
SI(ft) = Screened Interval, feet
TD(ft) = Total Depth, feet
2010

## Slide 22: Calvert Bluff Formation DFC Wells
State Well Number | Well Owner
39-54-703 | Private
59-03-438 | Private
59-03-606 | Private
59-06-104 | Private
Arithmetic Average | 8 Feet (Decline)
Spatially Weighted Average | --
Average Artesian Head Change 2000-2026
Arithmetic Average | 5 Feet (Decline)
Spatially Weighted Average | --
Average Artesian Head Change 2010-2026
2070 DFC | 111 Feet (Decline)

## Slide 23: Calvert Bluff Formation
Average Artesian Head Change 2000-2026
Average Artesian Head Change 2010-2026
2000-2026
Arithmetic Average: 8 feet (Decline)
Spatially Weighted Average: --
2010-2026
Arithmetic Average: 5 feet (Decline)
Spatially Weighted Average: --
DFC (2070):
111 feet Decline

## Slide 24: Calvert Bluff Formation Observation Wells
SWN = State Well Number
SI(ft) = Screened Interval, feet
TD(ft) = Total Depth, feet
2010

## Slide 25: Simsboro Aquifer DFC Wells
State Well Number | Well Owner
39-46-702 | Private
39-52-504 | Private
39-53-703 | Private
39-59-601 | Private
39-59-905 | Private
39-61-706 | City of Franklin Well 4
59-03-437 | Private
59-04-701 | City of Hearne Well 4
59-05-901 | Wickson Creek SUD Wheelock Well
59-14-706 | Wickson Creek SUD Well 1
59-21-412 | City of Bryan Well 19
59-21-714 | TAMU Well 8
Arithmetic Average | 73 Feet (Decline)
Spatially Weighted Average | 76 Feet (Decline)
Average Artesian Head Change 2000-2026
Arithmetic Average | 51 Feet (Decline)
Spatially Weighted Average | 55 Feet (Decline)
Average Artesian Head Change 2010-2026
2070 DFC | 262 Feet (Decline)

## Slide 26: Simsboro Aquifer
Average Artesian Head Change 2000-2026
Average Artesian Head Change 2010-2026
2000-2026
Arithmetic Average: 73 feet (Decline)
Spatially Weighted Average: 76 Feet (Decline)
2010-2026
Arithmetic Average: 51 feet (Decline) Spatially Weighted Average: 55 Feet (Decline)
DFC (2070):
262 feet Decline

## Slide 27: Spatially Weighted Simsboro Aquifer Head Change Estimates
TWDB Down Dip Limit of the Carrizo-Wilcox (3,000 mg/l TDS)
Weighted Average Artesian Head Change 2000-2026:
76 feet (Decline)
TWDB Down Dip Limit of the Carrizo-Wilcox (3,000 mg/l TDS)
Weighted Average Artesian Head Change 2010-2026:
55 feet (Decline)

## Slide 28: Simsboro Aquifer Observation Wells (Robertson County)
SWN = State Well Number
SI(ft) = Screened Interval, feet
TD(ft) = Total Depth, feet
2000
2010

## Slide 29: Simsboro Aquifer Observation Wells (Brazos County)
SWN = State Well Number
SI(ft) = Screened Interval, feet
TD(ft) = Total Depth, feet
2000
2010

## Slide 30: Hooper Formation DFC Wells
State Well Number | Well Owner
39-44-904 | Private
39-51-805 | Private
39-51-910 | City of Bremond Well 4
39-51-911 | City of Bremond Well 5
39-53-403 | Oak Grove Luminant Well 1
39-59-104 | Private
Arithmetic Average | 18 Feet (Decline)
Spatially Weighted Average | --
Average Artesian Head Change 2000-2026
Arithmetic Average | 5 Feet (Decline)
Spatially Weighted Average | --
Average Artesian Head Change 2010-2026
2070 DFC | 167 Feet (Decline)

## Slide 31: Hooper Formation
Average Artesian Head Change 2000-2026
Average Artesian Head Change 2010-2026
2000-2026
Arithmetic Average: 18 feet (Decline)
Spatially Weighted Average: --
2010-2026
Arithmetic Average: 5 feet (Decline)
Spatially Weighted Average: --
DFC (2070):
167 feet Decline

## Slide 32: Hooper Formation Observation Wells
SWN = State Well Number
SI(ft) = Screened Interval, feet
TD(ft) = Total Depth, feet

## Slide 33: Yegua-Jackson Aquifer DFC Wells
State Well Number | Well Owner
59-22-511 | Private
59-22-601 | Private
59-30-207 | TAMU Golf Course
59-21-911 | Private
59-30-308 | Wellborn SUD Well 1
59-30-410 | TAMU Brayton Training Field
59-31-703 | Private
Arithmetic Average | 0 Feet
Spatially Weighted Average | 0 Feet
2070 DFC | 67 Feet (Decline)
Average Artesian Head Change 2010-2026

## Slide 34: Yegua-Jackson Aquifer
Arithmetic Average | 0 Feet
Spatially Weighted Average | 0 Feet
2070 DFC | 67 Feet (Decline)
Average Artesian Head Change 2010-2026

## Slide 35: Yegua-Jackson Aquifer Observation Wells
SWN = State Well Number
SI(ft) = Screened Interval, feet
TD(ft) = Total Depth, feet

## Slide 36: Comparison of DFCs Over Last Seven Years, arithmetic average feet of artesian head change
Span of Years | Sparta | Queen City | Carrizo | Calvert Bluff | Simsboro | Hooper | Yegua- Jackson (2010)
2000-2020 | -7 | - | -20 | - | -33 | -8 | +6
2000-2021 | -9 | - | -7 | - | -34 | -14 | +11
2000-2022 | -12 | - | -11 | - | -43 | -6 | +8
2000-2023 | -16 | - | -14 | - | -58 | -5 | +9
2000-2024 | -17 | - | -13 | - | -66 | -11 | +7
2000-2025 | -12 | - | -14 | - | -68 | -22 | +7
2000-2026 | -11 | -8 | -21 | -8 | -73 | -18 | 0
DFC 2000-2070 (water level decline) | -53 | -44 | -84 | -111 | -262 | -167 | -67

## Slide 37: Comparison of DFCs arithmetic average feet of artesian head change from 2010 - 2026
Span of Years | Sparta | Queen City | Carrizo | Calvert Bluff | Simsboro | Hooper | Yegua- Jackson
2010-2026 | -3 | -3 | -19 | -5 | -51 | -5 | 0
DFC 2000-2070 (water level decline) | -53 | -44 | -84 | -111 | -262 | -167 | -67

## Slide 38: Comparison of Simsboro DFCs and Rate of Decline Over Last Seven Years
Span of Years | Simsboro Arithmetic Average Artesian Head Change, feet | Simsboro Rate of Decline During Current Year based on Arithmetic Average, feet | Simsboro Spatially Weighted Average Artesian Head Change, feet | Simsboro Rate of Decline During Current Year based on Spatially Weighted Average, feet
2000-2020 | -33 | - | -33 | -
2000-2021 | -34 | 1 | -35 | 2
2000-2022 | -43 | 9 | -43 | 8
2000-2023 | -58 | 15 | -59 | 16
2000-2024 | -66 | 8 | -68 | 9
2000-2025 | -68 | 2 | -70 | 2
2000-2026 | -73 | 5 | -76 | 6
DFC (2000-2070) | -262 |  |  | 

## Slide 39
Chart: 
DFC | -28 | -31 | -32 | -33 | -34 | -43 | -58 | -66 | -68 | -73
2000
to
2026
2000
to
2025
2000
to
2024
2000
to
2023
2000
to
2022
2000
to
2021
2000
to
2020
2000
to
2019
2000
to
2018
2000
to
2017
BVGCD GMA 12 2021 Simsboro DFC: 2000 to 2070: -262 feet
Comparison of the Simsboro Aquifer Average Artesian Head Change and DFC
Arithmetic average of artesian head change (feet)

## Slide 40: Brazos River Alluvium Aquifer DFC Wells
State Well Number | Well Owner
59-03-402 | Private
59-11-309 | Private
59-12-420 | Private
59-12-807 | Private
59-20-907 | Private
59-38-608 | Private
59-39-809 | Private

## Slide 41: Location of Brazos River Alluvium Wells with Water Level Hydrographs

## Slide 42: Brazos River Alluvium Observation Wells (Robertson County)
SWN = State Well Number
TD(ft) = Total Depth, feet

## Slide 43: Brazos River Alluvium Observation Wells (Brazos County)
SWN = State Well Number
TD(ft) = Total Depth, feet

## Slide 44: Brazos River Alluvium Well Data
Hwy 21
WD = Well Depth, ft
DTW = Depth to Water, ft
Percent Saturation (PS)= WD-DTW
WD
2021 | 2022 | 2023 | 2024 | 2025 | 2026
68% | 69% | 63% | 64% | 64% | 66%
2070 DFC
Percent Saturation
≥ 30% North of Hwy 21
and
≥ 40% South of Hwy 21
Arithmetic Average Percent Saturation

## Slide 45: Summary
The rate of average artesian head decline slightly increase in the Simsboro in 2026
District staff continues to add wells to monitoring network
Continue to review District well and water level records to add additional data for use in DFC analysis

## Slide 46: Questions?

## Slide 47: Simsboro Aquifer Pumping Estimates: 2009 Through 2025 (draft)